## Slide 1
Security Engineering – Physical Security

## Slide 2: Secure Facility Plan
Critical Path Analysis:
  Systematic effort to identify relationships between mission-critical applications, processes
  When performing this analysis technology convergence should be taken into consideration
Technology Convergence:
  Tendency of various technologies, solutions, utilities and systems to evolve and merge over time
The primary goal of the plan should be to protect human life.
Life safety goals should take precedence over all other types of goals
Notes: How presentation will benefit audience: Adult learners are more interested in a subject if they know how or why it is important to them.
Presenter’s level of expertise in the subject: Briefly state your credentials in this area, or explain why participants should listen to you.

## Slide 3: Threats to an organization
  4 Main threats categories to an organization are
    Natural environmental threats
      Flood, earthquakes etc
    Supply system threats
      Power distribution failure, communications interruption
    Manmade threats
      Unauthorized access, fraud, theft, errors, accidents
    Socio-political threats
      Strikes, war, violence, terrorist attack
Notes: How presentation will benefit audience: Adult learners are more interested in a subject if they know how or why it is important to them.
Presenter’s level of expertise in the subject: Briefly state your credentials in this area, or explain why participants should listen to you.

## Slide 4: Physical Security Program Goals
Prevention through Deterrence
  Fence, security guard, dogs
Damage reduction through Delay
  Security layer, barriers
Anomaly Detection
  CCTV, smoke detectors, alarms
Incident Analysis
  Response to detect events, triage
Response to Incident
  Fire suppression, emergency response, Law enforcement notification

## Slide 5: Crime Prevention through Environmental Design
Discipline that outlines how proper design of physical environment can reduce crime by directly affecting human behavior
Three main strategies of CPTED are
  Natural access control
  Natural surveillance
  Natural territorial reinforcement
Best physical security approach is to build an environment from a CPTED approach and apply target hardening principles on top of the design
Target Hardening
  Focusses on denying access through physical and artificial barriers
  It can lead to restrictions on the use and aesthetics of an environment.

## Slide 6: Natural Access control
Guidance of people entering/leaving a space by placement of doors, fences, lighting and even landscaping
Clear line of sight, transparency via glass
Creation of security zones, layering different security levels and applying specific controls per zone
Create barriers
  Natural – cliff, river, hill
  Manmade – highway; railway line
  Artificial - fences, closing streets

## Slide 7: Natural Surveillance
Can take place through
  Organized means (security guards)
  Mechanical means (CCTV)
  Natural strategies (clear line of sight, low landscaping)
Main objective is to give the maximum visibility to activity areas thereby preventing malicious actions

## Slide 8: Natural Territorial Reinforcement
Creates physical designs that emphasizes the companies physical sphere of influence so legitimate users feel a sense of ownership
Can be implemented through, fence, landscaping, sing-boards, flags
Goal is to create a sense of dedicated community

## Slide 9: Construction Material
Light frame material | Composed of untreated lumber that is combustible during fire Provides least amount of protection Used to build houses Fire survival rate is 30 minutes
Heavy Timber | The material must be at least 4 inches in thickness Denser wood is used and are fastened with metal bolts Fire survival rate is 1 hour Commonly used for office building
Incombustible material | Provides higher level of protection against combustion, but loses its strength under extreme temperature Eg: Steel
Fire-resistance material | Construction material is fire retardant Steel rods are cased inside a concrete wall and support beams Provides the most protection against fire and forced entry attempts

## Slide 10: Entry Points
They are the weakest section of the structure; made of doors and windows
In doors the weakness lies within the frames, hinges and door material
The door and surrounding walls and ceilings should also provide the same level of strength

## Slide 11: Door Types
Hollow-core:
  Can be easily penetrated by cutting or kicking them
  Should not be used in exterior places
Solid-core:
  Stronger than hollow-core, has a higher fire rating and protection from forced entry
  Can be used externally
Bulletproof doors
  Bullet-resistant and bulletproof material is sandwiched between wood or steel
  High protection areas can have bullet proof doors

## Slide 12: Door Types
Turnstile
  Form of door that prevents more than one person entering at a time
  Coupled with security guards/access control helps prevent un-authorized entry into facility
  Can prevent tailgating
Mantrap
  A set of double doors often protected by a guard
  The first door is provided access for entry, once the person passes the first door and enters, the first door closes; the person has to authenticate again at the second door to get access
  This prevents piggybacking and tailgating

## Slide 13: Window types
Standard | Common type, cheapest and lowest protection
Tempered | Glass is heated and suddenly cooled to increase its integrity and strength
Acrylic | A type of plastic, polycarbonate acrylics are stronger than normal acrylic
Wired | A mesh of wire is embedded between the glass; prevents the glass from shattering
Laminated | Plastic layer is placed between the glasses; helps increase its strength
Security Film | Transparent film is applied to the glass to increase strength and obscure visibility

## Slide 14: Equipment Failure
Establishing SLA with vendor is essential
  SLA defines the response time the vendor will provide in the event of an equipment failure
MTTF – Mean time to Failure
  Typical functional life time of the device given a specific operating environment
MTTR – Mean time to Repair
  Average length of time required to perform a repair on the device
MTBF – Mean time between Failure
  Estimation of time between the first and any subsequent failures

## Slide 15: Datacentre security
Datacenter, server rooms, wiring closets should be located in the core of the facility
Wiring closets in a multistory building should be placed directly above or below each other; this helps easier connectivity of wires across the building
Access to DC should be via only one door; if additional doors are there, they should function as one-way exit doors
DC should not be located in the basement or upper floors of a building
Should be located well above the ground level
Data processing center should be constructed as one room rather than different individual rooms
Should have positive air pressure ~ no contaminants can be sucked into the room
Water detectors should be placed under raised floors and on dropped ceilings
HVAC system should be implemented for temperature and humidity control

## Slide 16: Media storage security - Safe
Safes are commonly used to store media
Passive locking safes can detect if someone attempts to tamper with it, in which case extra internal bolts will fall into place to ensure it cannot be compromised
Thermal locking safes can identify temperature changes and implement additional locks
Wall Safe | Embedded into the wall and easily hidden
Floor Safe | Embedded into the floor and easily hidden
Chests | Stand alone safe
Depositories | Safes with slots, allows valuables to be slipped in
Vaults | Safes that are large enough to allow walk-in

## Slide 17: Access control
Smartcards:
  Security ID with embedded magnetic strip, bar code, or integrated circuit chip.
  Can process information or store reasonable amount of data in memory
  Can be used in multifactor authentication for better protection
  Vulnerable to physical security attacks
Memory cards
  Machine readable ID cards with memory sticks
  Can hold small amount of data in memory but cannot process it
  Memory cards are easy to copy or duplicate
Proximity readers
  Passive device, or transponder that can be used to control physical access
  A passive device, typically worn by an individual alters the magnetic field generated by the reader which is detected and processed

## Slide 18: Motion Detectors
A device that senses movement or sound in a specific area
Type | Operation
Infrared | Monitors for significant changes in infrared lighting pattern of a monitored area
Heat-based | Monitors for significant changes in heat levels of a monitored area
Wave pattern | Transmits low ultrasonic frequency signal and monitors for significant changes in the reflected patters
Capacitance | Monitors the changes in electrical or magnetic field surrounding a monitored object
Photoelectric | Monitors visible light levels in a monitored area
Passive audio | Listens for abnormal sounds in monitored area

## Slide 19: Electric Power – Power Protection
Power can be protected in 3 ways
  UPS, Power line conditioners, backup sources
UPS: Battery packs that can range in size and capacity
Online UPS –
  uses AC voltage to charge the batteries, uses inverter to change the DC output from the batteries to AC form
  Normal power always passes through them, hence it detects power failure much faster
  Constantly provide power from their own inverters, even when the electric power is in proper use
Standby UPS
  Stays inactive until electric power failure
  Has sensors to detect a power failure and the load is switched to the battery pack

## Slide 20: Electric Power – Power Issues
Clean power:
  Power supply does not contain any interference or voltage fluctuation
  Interference can be via EMI or RFI
EMI (Noise):
  Can be created by difference in the 3 wires: neutral, hot, ground and the magnetic field they create
  Common mode noise: generated by difference in power between hot and ground
  Traverse mode noise: generated by difference in power between hot and neutral
  Lightning and electrical motors can induce EMI
RFI
  Can be caused by anything that creates radio waves
  Fluorescent lighting is one of the main causes of RFI within buildings today

## Slide 21: Electric Power – Problems
Power Excess | Spike | Momentary high voltage
 | Surge | Prolonged high voltage
Degradation | Sag/dip | Momentary low voltage
 | Brownout | Prolonged low voltage
 | In-rush current | Initial surge of current required to start load
Power Loss | Fault | Momentary power outage
 | Blackout | Prolonged power outage
Interference | Transient | A short duration of line noise disturbance
 | Noise | Stead interfering power disturbance or fluctuation

## Slide 22: Emanation Security
Preventing unauthorized intercept of EMI or RF signals from the devices
TEMPEST is used to protect against emanation leaks
TEMPEST countermeasures include Farady cage, white noise, control zones
  Faraday Cage:
    A closed enclosure with external metal mesh that fully surrounds the enclosure absorbing EM signals
    They are quite effective in blocking EM signals
  White Noise:
    Broadcasting false traffic at all times to mask and hide presence of real emanations
    Most effective when created around the perimeter of an area so that it is broadcast to protect the internal area where emanations may be needed
  Control Zones
    Implementation of zones such that the emanations are controlled within the environment; can use faraday cage or white noise in those zones

## Slide 23: HVAC
Humidity should be between 40 to 60 % for Datacenter
High humidity will cause corrosion
Low humidity will cause static electricity
Damaging Temperature | Component
175F | Computer systems
100F | Magnetic storage devices
350F | Paper products
Static voltage | Possible damage
40 | Sensitive circuits and electronic components
1500 | Data stored in hard drives
2000 | Abrupt system shutdown

## Slide 24: Fire Prevention, Detection and Suppression
Fire Prevention
  Training employees of fire safety
  Supplying right equipment and ensuring their working condition
  Storing combustible material in a proper manner
Fire Detection
  Fire detectors placed at strategic points to detect smoke/fire
Fire Suppression Systems
  Use of suppression agent to put out a fire

## Slide 25: Stages of Fire
Stage 1 – Incipient stage | Initial Stage, only air ionization, no smoke
Stage 2 – Smoke stage | Smoke is visible from the point of ignition
Stage 3 – Flame stage | Flame can be seen with naked eye
Stage 4 – Heat stage | Fire is considerably higher
The earlier the fire is detected, the easier it is to be extinguished

## Slide 26: Fire Detection
Smoke Activated
  Good early warning devices
  Photoelectric device
    Detects variation in light intensity – produces a beam of light and if the light is obstructed an alarm is produced
Heat Activated
  Fixed temperate: Alarm is generated when a particular temperate us reached
  Rate-of-raise: alarm is generated when temperature raises over time
  Rate-of-raise temperature sensors usually provide a quicker warning that fixed-temperature sensors but they are prone to false positives

## Slide 27: Fire Suppression
Fire Class | Type of Fire | Elements | Suppression Method
A | Common Combustible | Wood, paper | Water, Foam
B | Liquid | Oil and coolants | Gas, CO2, Foam, Dry Powder
C | Electrical | Wires, Electrical equipment's | Gas, CO2, Dry Powder
D | Metals | Magnesium, sodium, potassium | Dry powder
CO2 should be used only in unattended areas
There should a delay mechanism before CO2 is released
FM200 is the approved replacement for Halon gas
Dry powder like potassium bicarbonate, calcium carbonate interrupt the chemical combustion of fire
Dry powder like mono-ammonium phosphate melts and low temperature and excludes oxygen from fuel

## Slide 28: Water based Fire Suppression
Type | Functionality | comment
Wet-pipe | It is always full of water, usually discharged by temperature control sensors Also called closed head systems | Water may freeze in colder temperatures A damage in nozzle or pipe can result in leak
Dry Pipe | Water is not stored in pipe, instead contains compressed air. Opening the water valve cause water to fill the pipes and discharge | Best suited for colder climates
Preaction | Combination of wet and dry pipe; water is not held in pipes until fire is detected; it is released only after the sprinkler head activation triggers are melted by sufficient heat; | Used in data processing equipment's
Deluge | Another form of dry pipe system that uses larger pipes and can deliver significantly larger volume of water | Inappropriate for environments that contain electronic equipments

## Slide 29: Gas Suppression
More effective than water suppression systems
Gas discharge systems removes oxygen in the air and hence should not be used in environments were people are located
Halon is an effective gas suppression system, but it degrades environment and hence is since banned
Effective replacement for Halon are
  FM200
  NAF-S-III
  Argon
  Inergen

## Slide 30: Intrusion Alarm
Alarm | Operation
Deterrent | Alarms that trigger deterrent actions; goal is to make intrusion attempts more difficult
Repellent | Alarms that trigger sound or light; goal is to discourage intruders
Notification Alarm | Alarms that trigger notifications to security analyst; they are silent from attacker perspective but gives warning signals to security team
Category | Operation
Local Alarm System | Must broadcast an audible alarm signal that can be heard within 400feet; for a local alarm to be effective security guards should be stationed nearby
Central Station | Alarm is silent locally, but offsite monitor agents are notified;
Auxiliary system | Can be added to either local or centralized system, notification is sent to emergency services including fire, police and medical teams

## Slide 31: Motion Detectors
Type | Operation
Infrared | Monitors for significant changes in the IR lighting pattern of a monitored area
Heat-based | Monitors for significant change in the heat levels in a monitored area
Wave pattern | Transmits a consistent low ultrasonic or high micros-wave frequency signal into a monitored area and monitors for significant changes in the reflected pattern
Capacitance | Senses changes in the EM signals or magnetic fields surrounding a monitored object
Photoelectric | Senses changes in the visible light levels for the monitored area. Usually deployed in internal rooms that have no windows and are kept dark
Passive Audio | Listens for abnormal sounds in the monitored area

## Slide 32
Karthikeyan Dhayalan
MD & Chief Security Partner
www.cyintegriti.com