## Slide 1
Network Foundations

## Slide 2: Network Topology
Manner in which a network is physically connected and shows the layout of resources and systems
Topological structure of a network depicted physically or logically
Types of topology
    Ring
    Star
    Bus
    Mesh
    Tree
    Hybrid
Notes: How presentation will benefit audience: Adult learners are more interested in a subject if they know how or why it is important to them.
Presenter’s level of expertise in the subject: Briefly state your credentials in this area, or explain why participants should listen to you.

## Slide 3: RING Topology
Closed loop unidirectional transmission links to which devices are serially connected
The transmission is unidirectional, but it can be made bidirectional by having 2 connections between each Network Node, it is called Dual Ring Topology
Data is transferred in a sequential manner that is bit by bit. Data transmitted, has to pass through each node of the network, till the destination node.
Advantage
  Transmitting network is not affected by high traffic or by adding more nodes, as only the nodes having tokens can transmit data
  Cheap to install and expand
Disadvantage
  Troubleshooting is difficult in ring topology
  Adding or deleting the computers disturbs the network activity
  Failure of one computer disturbs the whole network
Notes: How presentation will benefit audience: Adult learners are more interested in a subject if they know how or why it is important to them.
Presenter’s level of expertise in the subject: Briefly state your credentials in this area, or explain why participants should listen to you.

## Slide 4: BUS Topology
Every computer and network device is connected to single cable
When it has exactly two endpoints, then it is called Linear Bus topology.
  Single cable with nodes attached
When there are branches from the single cable, it is called Tree topology
It transmits data only in one direction
Every device is connected to a single cable
Advantages
  cost effective / easy to understand / Used in small networks.
  Easy to expand joining two cables together / Cable required is least compared to other network topology
Disadvantages
  Cables fails then whole network fails
  If network traffic is heavy or nodes are more the performance of the network decreases.
  Cable has a limited length
  It is slower than the ring topology
Notes: How presentation will benefit audience: Adult learners are more interested in a subject if they know how or why it is important to them.
Presenter’s level of expertise in the subject: Briefly state your credentials in this area, or explain why participants should listen to you.

## Slide 5: STAR Topology
All the computers are connected to a central node
Every node has its own dedicated connection to the central node
The central node acts as a repeater for data flow
Can be used with twisted pair, Optical Fibre or coaxial cable
Advantages
  Fast performance with few nodes and low network traffic
  Central nodes can be upgraded easily
  Easy to setup, deploy and troubleshoot
  Failure of one system does not negatively impact the network
Disadvantages
  Cost of installation is high and expensive to use
  If central node fails then the whole network is stopped
  Performance is based on the central node that is it depends on its capacity
Notes: How presentation will benefit audience: Adult learners are more interested in a subject if they know how or why it is important to them.
Presenter’s level of expertise in the subject: Briefly state your credentials in this area, or explain why participants should listen to you.

## Slide 6: MESH Topology
It is a point-to-point connection to other nodes or devices. All the network nodes are connected to each other.
There are two techniques to transmit data over the Mesh topology, they are :
  Routing: the nodes have a routing logic, as per the network requirements
  Flooding: the same data is transmitted to all the network nodes, hence no routing logic is required
Partial Mesh Topology : In this topology some of the systems are connected in the same fashion as mesh topology but some devices are only connected to two or three devices.
Full Mesh Topology : Each and every nodes or devices are connected to each other.
Advantages
  Each connection can carry its own data load
  Provides security and privacy
Disadvantage
  Installation and configuration is difficult
  Bulk wiring is required
Notes: How presentation will benefit audience: Adult learners are more interested in a subject if they know how or why it is important to them.
Presenter’s level of expertise in the subject: Briefly state your credentials in this area, or explain why participants should listen to you.

## Slide 7: TREE Topology
It has a root node and all other nodes are connected to it forming a hierarchy. It is also called hierarchical topology.
Used in WAN
Ideal if workstations are located in groups
Advantages
  Extension of bus and star topologies
  Expansion of nodes is possible and easy
  Easily managed and maintained
  Error detection is easily done
Disadvantages
  Heavily cabled
  Costly
  If more nodes are added maintenance is difficult
  Central hub fails, network fails
Notes: How presentation will benefit audience: Adult learners are more interested in a subject if they know how or why it is important to them.
Presenter’s level of expertise in the subject: Briefly state your credentials in this area, or explain why participants should listen to you.

## Slide 8: Media Access Technologies

## Slide 9: General Introduction
Deals with how systems communicate over the media
It is usually represented in protocols, NIC drivers and interfaces
They setup the rules
  on how systems communicate in a network,
  how errors are handled
  The MTU – Maximum transmission unit
    How much data a frame can carry on a specific network
Some of the Media Access technologies are
  Ethernet
  Token Ring
  FDDI

## Slide 10: Token Passing Access method
A token (24-bit control frame) decides which computer can communicate and at what intervals
Only the computer having a token can send data
Other computers have to wait for their turn
Only the computer that sent the data can remove the data from the token and release it; destination computer can only copy the data
Does not have issue with collisions
Token Ring, FDDI protocols use this method

## Slide 11: CSMA
Carrier Sense multiple access protocol is used by Ethernet
Two types
  CSMA/CD
  CSMA/CA
CSMA/CD
  Systems monitor the network for transmission activity; if they sense the network to be free; the computer transmits the data
  If two systems send the data at the same time, collision occurs
  In a network with highly populated network, damaged cable or connector, cables exceeding the recommended value cause too many collisions
  If collision happens the devices in the network execute a random collision timer to force a delay before they attempt to transmit data. This timer is called back-off algorithm

## Slide 12: CSMA
CSMA/CA
  Systems monitor the network for transmission activity; if they sense the network to be free; the computer beacons out a broadcast message before transmitting the data
  This is primarily used in Wireless LAN Technology

## Slide 13: Collision and Broadcast domain
Collision Domain
  Is a group of computers that are contending for the same shared communication medium
  Collision domains are there in network that are connected by a hub, repeater or wireless access points
Broadcast Domain
  Set of computing nodes that can receive all layer 2 broadcast frames
  They are nodes interconnected by switches, bridges or hubs but with no router in between them

## Slide 14: Polling
Used by mainframe environments
The systems are divided into primary stations and secondary stations
Primary stations poll the secondary stations at regular intervals to check for any data transmission. This is the only time secondary station can communicate

## Slide 15: Ethernet
A set of technologies that enable several devices to communicate on the same network
Usually uses bus or star topology
It is defined by 802.3 Standard
It is contention-based technology
Uses Collision and broadcast domains
Uses CSMA/CD
Supports full duplex communication
Uses coaxial, twisted pair, fibre-optic cabling types

## Slide 16: Token Ring
LAN media access technology developed by IBM
Defined by 802.5 standard
Has data transmission rate upto 16Mbps
Uses token passing technology with star-configured topology
Each computer is connected to the central hub MAU (Multiple Access Unit)
Active monitor is used to remove frames that are continuously circulating the network
Beaconing mechanism will ensure if a computer detects a problem it sends a beacon frame
This frame generates a failure domain, which is between the computer that issued the beacon and its neighbour downstream.

## Slide 17: FDDI
High speed, token passing media access technology works on Fiber-optic cabling
Has transmission speed upto 100Mbps
Provides fault tolerance by providing a secondary counter-rotating ring
It is primarily used in backbone networks (MAN)
Can be deployed for distances up to 100Kms
Devices fall into the following criteria
  Single-attachment station (SAS) – attaches to only one ring through a concentrator
  Single-attached concentrator (SAC) – connects a SAS device to the primary ring
  Dual-attachment station (DAS) – has two ports, each port provides a connection for both the primary and secondary rings
  Dual-attached concentrator (DAC) – concentrator that connects DAS, SAS, and SAC devices to both the rings
FDDI-2 provides fixed bandwidth – makes it work like a broadband connection with QoS capabilities.
Copper Distributed Data Interface (CDDI) – work over UTP and used in LAN environments

## Slide 18: Transmission Methods
Unicast – one to one
Broadcast – one to all
Multicast – one to many (Layer 3)
IGMP is used to report multicast group membership to routers
IGMP can be used for online streaming and video activities

## Slide 19: Network Protocols and Services

## Slide 20: Address Resolution Protocol (ARP)
ARP finds the hardware address, also known as Media Access Control (MAC) address, of a host from its known IP address.
The protocol operates below the network layer as a part of the interface between the OSI network and OSI link layer.

## Slide 21: ARP cache poisoning
By 0x55534C - Own work, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=15034709
ARP spoofing, ARP cache poisoning, or ARP poison routing, is a technique by which an attacker sends (spoofed) Address Resolution Protocol (ARP) messages onto a local area network.
The attack can only be used on networks that use the Address Resolution Protocol, and is limited to local network segments

## Slide 22: DHCP
Runs over UDP
Utilizing ports:
  67 – connections to server
  68 – connections to client
Extension of BOOTP (protocol used for simple interaction)
Uses client–server model
All interactions are initiated by a client
Server only replies
Client broadcasts DHCPDISCOVER
One or more servers return DHCPOFFER with available Address and NW Information
Client chooses one offer that it likes best
broadcasts DHCPREQUEST to identify chosen Server/lease
DHCPREQUEST also to renew lease
DHCP Snooping:
  Ensures server can allocate IP address only to those systems that are identified by their MAC address
Server sends
  DHCPACK
    Lease is finalized
    Client starts using IP
  DHCPNAK
    Client resumes from DHCPDISCOVER point
If client doesn’t want IP - DHCPDECLINE is sent
DHCPRELEASE gives IP back into pool

## Slide 23: RARP and BOOTP
RARP (Reverse Address Resolution Protocol) is a protocol by which a physical machine in a local area network can request to learn its IP address from a gateway server's Address Resolution Protocol (ARP) table or cache.
An RARP server attached to the physical network normally provides the mapping from a hardware address to an IP address for many hosts
As with ARP requests, RARP requests are sent as hardware (Ethernet) level broadcasts. Thus the server must be present on the same physical network as the diskless workstation
RARP only provides an IP address to a host
BOOTP has been used for Unix-like diskless workstations to obtain the network location of their boot image, in addition to the IP address assignment.
BOOTP was the predecessor of the Dynamic Host Configuration Protocol, successor to RARP
  It is still based on a client/server exchange, but is implemented as a higher-layer software protocol, using UDP for message transport. It is not dependent on the particular hardware of the network like RARP.
  It supports sending additional configuration information to a client beyond just an IP address. This extra information can usually all be sent in one message for efficiency.
  It can handle having the client and server on different networks of an internetwork. This allows the administration of the server providing IP addresses to be more centralized, saving money as well as administrative time and hassle.

## Slide 24: ICMP
Internet Control Message Protocol (ICMP) is the component of the TCP/IP protocol stack that addresses this basic limitation of IP.
ICMP does not overcome the unreliability issues in IP.
Reliability must be provided by upper layer protocols if it is needed
ICMP is an error reporting protocol for IP.
When datagram delivery errors occur, ICMP is used to report these errors back to the source of the datagram.
ICMP does not correct the encountered network problem; it merely reports the problem.
ICMP reports on the status of the delivered packet only to the source device.
It does not propagate information about network changes to routers.

## Slide 25: SNMP
Client server protocol used to view status of the network, traffic flows, and the hosts within the network
Uses UDP 161 and 162 for communication
Two main components
  Manager – server portion, that polls the agent at regular intervals to check status information
  Client – software installed in agents, collects information on various parameters of the system (MIB) and share it with the manager when requested for. Clients use trap message to alert Manager when specific parameters changes. That is the only time when a client will respond to manager without polling
Communities are used to create trust between the manager and agent
Two community strings are used
  Public – read-only; allows manager to read the data stored in MIB
  Private – read-write; allows manager to read and modify the data in MIB
Community strings should be strong
V1 and V2 send community strings in plain text, hence it is important to use V3

## Slide 26: DNS
The mechanism by which Internet software translates names to attributes such as addresses
A globally distributed, scalable, reliable database
Comprised of three components
  A “name space”
  Servers making that name space available
  Resolvers (clients) which query the servers about the name space
The name space is the structure of the DNS database
  An inverted tree with the root node at the top
Each node has a label
  The root node has a null label, written as “”
A domain name is the sequence of labels from a node to the root, separated by dots (“.”s), read left to right
  The name space has a maximum depth of 127 levels
  Domain names are limited to 255 characters in length
A node’s domain name identifies its position in the name space

## Slide 27: Subdomain
One domain is a subdomain of another if its domain name ends in the other’s domain name
  So sales.nominum.com is a subdomain of
    nominum.com & com
  nominum.com is a subdomain of com
nominum.com domain
nominum.com zone
ams.nominum.com zone
rwc.nominum.com zone
Acknowledgement: David Conrad at nominum.com

## Slide 28: Name Servers
Name servers store information about the name space in units called “zones”
  The name servers that load a complete zone are said to “have authority for” or “be authoritative for” the zone
Usually, more than one name server are authoritative for the same zone
  This ensures redundancy and spreads the load
Also, a single name server may be authoritative for many zones
128.8.10.5
nominum.com
204.152.187.11
202.12.28.129
Name Servers
isc.org
Zones
128.8.10.5 serves data for both nominum.com and isc.org zones
202.12.28.129 serves data for nominum.com zone only
204.152.187.11 serves data for isc.org zone only
Acknowledgement: David Conrad at nominum.com

## Slide 29: Name Servers
Two main types of servers
  Authoritative – maintains the data
    Master – where the data is edited
    Slave – where data is replicated to
  Caching – stores data obtained from an authoritative server
You can think of a name server as part of:
  database server, answering queries about the parts of the name space it knows about (i.e., is authoritative for),
  cache, temporarily storing data it learns from other name servers, and
  agent, helping resolvers and other name servers find data

## Slide 30: Name Resolution
A DNS query has three parameters:
  A domain name (e.g., www.nominum.com),
  Remember, every node has a domain name!
  A class (e.g., IN), and
  A type (e.g., A)
Upon receiving a query from a resolver, a name server
  1) looks for the answer in its authoritative data and its cache
  2) If step 1 fails, the answer must be looked up

## Slide 31: The Resolution Process
ping www.nominum.com.
Let’s look at the resolution process step-by-step:
annie.west.sprockets.com
Acknowledgement: David Conrad at nominum.com

## Slide 32: The Resolution Process
What’s the IP address of www.nominum.com?
The workstation annie asks its configured name server, dakota, for www.nominum.com’s address
ping www.nominum.com.
annie.west.sprockets.com
dakota.west.sprockets.com
Acknowledgement: David Conrad at nominum.com

## Slide 33: The Resolution Process
The name server dakota asks a root name server, m, for www.nominum.com’s address
ping www.nominum.com.
annie.west.sprockets.com
m.root-servers.net
dakota.west.sprockets.com
What’s the IP address of www.nominum.com?
Acknowledgement: David Conrad at nominum.com

## Slide 34: The Resolution Process
The root server m refers dakota to the com name servers
This type of response is called a “referral”
ping www.nominum.com.
annie.west.sprockets.com
m.root-servers.net
dakota.west.sprockets.com
Here’s a list of the com name servers. Ask one of them.
Acknowledgement: David Conrad at nominum.com

## Slide 35: The Resolution Process
The name server dakota asks a com name server, f, for www.nominum.com’s address
ping www.nominum.com.
annie.west.sprockets.com
m.root-servers.net
dakota.west.sprockets.com
What’s the IP address of www.nominum.com?
f.gtld-servers.net
Acknowledgement: David Conrad at nominum.com

## Slide 36: The Resolution Process
The com name server f refers dakota to the nominum.com name servers
ping www.nominum.com.
annie.west.sprockets.com
f.gtld-servers.net
m.root-servers.net
dakota.west.sprockets.com
Here’s a list of the nominum.com name servers. Ask one of them.
Acknowledgement: David Conrad at nominum.com

## Slide 37: The Resolution Process
The name server dakota asks a nominum.com name server, ns1.sanjose, for www.nominum.com’s address
ping www.nominum.com.
annie.west.sprockets.com
f.gtld-servers.net
m.root-servers.net
dakota.west.sprockets.com
ns1.sanjose.nominum.net
What’s the IP address of www.nominum.com?
Acknowledgement: David Conrad at nominum.com

## Slide 38: The Resolution Process
The nominum.com name server ns1.sanjose responds with www.nominum.com’s address
ping www.nominum.com.
annie.west.sprockets.com
f.gtld-servers.net
m.root-servers.net
dakota.west.sprockets.com
ns1.sanjose.nominum.net
Here’s the IP address for www.nominum.com
Acknowledgement: David Conrad at nominum.com

## Slide 39: The Resolution Process
Here’s the IP address for www.nominum.com
The name server dakota responds to annie with www.nominum.com’s address
ping www.nominum.com.
annie.west.sprockets.com
f.gtld-servers.net
m.root-servers.net
dakota.west.sprockets.com
ns1.sanjose.nominum.net
Acknowledgement: David Conrad at nominum.com

## Slide 40: Resolution Process (Caching)
ping ftp.nominum.com.
After the previous query, the name server dakota now knows:
  The names and IP addresses of the com name servers
  The names and IP addresses of the nominum.com name servers
  The IP address of www.nominum.com
Let’s look at the resolution process again
annie.west.sprockets.com
Acknowledgement: David Conrad at nominum.com

## Slide 41: Resolution Process (Caching)
ping ftp.nominum.com.
What’s the IP address of ftp.nominum.com?
The workstation annie asks its configured name server, dakota, for ftp.nominum.com’s address
annie.west.sprockets.com
f.gtld-servers.net
m.root-servers.net
dakota.west.sprockets.com
ns1.sanjose.nominum.net
Acknowledgement: David Conrad at nominum.com

## Slide 42: Resolution Process (Caching)
ping ftp.nominum.com.
What’s the IP address of ftp.nominum.com?
dakota has cached a NS record indicating ns1.sanjose is an nominum.com name server, so it asks it for ftp.nominum.com’s address
annie.west.sprockets.com
f.gtld-servers.net
m.root-servers.net
dakota.west.sprockets.com
ns1.sanjose.nominum.net
Acknowledgement: David Conrad at nominum.com

## Slide 43: Resolution Process (Caching)
ping ftp.nominum.com.
Here’s the IP address for ftp.nominum.com
The nominum.com name server ns1.sanjose responds with ftp.nominum.com’s address
annie.west.sprockets.com
f.gtld-servers.net
m.root-servers.net
dakota.west.sprockets.com
ns1.sanjose.nominum.net
Acknowledgement: David Conrad at nominum.com

## Slide 44: Resolution Process (Caching)
ping ftp.nominum.com.
Here’s the IP address for ftp.nominum.com
The name server dakota responds to annie with ftp.nominum.com’s address
annie.west.sprockets.com
f.gtld-servers.net
m.root-servers.net
dakota.west.sprockets.com
ns1.sanjose.nominum.net
Acknowledgement: David Conrad at nominum.com

## Slide 45: DNS Attacks
DNS cache poisoning
  These attacks capture and divert queries to another website unknown to users
Denial of service (DoS)
  Attempts to make a given service impossible or very hard to access. Attacks sometimes use brute force (saturating servers by flooding them with simultaneous queries) or go for a more subtle approach by exhausting a rare resource on the server
Distributed denial of service (DDoS)
  An elaborate form of DoS that involve thousands of computers generally as part of a botnet or robot network: a network of zombie computers that the attacker commandeers from their unwitting owners by spreading malware from one machine to another
Reflected attacks
  send thousands of requests with the victim’s name as the source address. When recipients answer, all replies converge on the official sender, whose infrastructures are then affected.

## Slide 46: DNS Attacks
Reflective amplification DoS:
  if the size of the answer is larger than the question, an amplification effect is caused. The same technique as reflected attacks is used, except that the difference in weight between the answer and question amplifies the extent of the attack. A variant can exploit the protective measures in place, which need time to decode the long replies; this may slow down query resolution
Cybersquatting
  involves registering a domain name with the deliberate intent of undermining and profiting from a third party’s rights or in some way harming that third party.
"Name-jacking" or theft
  appropriating the domain name (updating the holder’s field and/or contacts) or taking control by technical means to divert traffic, such as by modifying the name servers hosting the site.

## Slide 47: SMTP
SMTP clients and servers have two main components
  User Agents – Prepares the message, encloses it in an envelope. (ex. Thunderbird, Eudora)
  Mail Transfer Agent – Transfers the mail across the internet (ex. Sendmail, Exim)
All Messages
POP3:
IMAP:
Dr.Amer
Friends
….
headers
Whole message
POP vs. IMAP
Internet
Internet

## Slide 48
Post Office Protocol v3
Simple
Allows the user to obtain a list of their Emails
Users can retrieve their emails
Users can either delete or keep the email on their system
Minimizes server resources

## Slide 49
Internet Mail Access Protocol v4
Has more features than POP3
User can check the email header before downloading
Emails can be accessed from any location
Can search the email for a specific string of characters before downloading
User can download parts of an email
User can create, delete, or rename mailboxes on a server

## Slide 50: Email Threats
Email Spoofing
  Modifying the fields in the email header so that the email appears to be from a trusted source
  Controls
    SMTP-AUTH
      The AUTH command is an ESMTP command (SMTP service extension) that is used to authenticate the client to the server. The AUTH command sends the clients username and password to the e-mail server.
    Sender Policy Framework (SPF)
      Allows administrators to specify which hosts are allowed to send emails from a given domain. This is done by creating a SPF record in DNS
Phishing Attack
  Spear Phishing
    Targets a particular set of population
  Whaling attack
    Target high profile individuals

## Slide 51: Network Address translation
NAT is a gateway between Internal private network and Internet that performs transparent routing and address translation
3 Basic types of NAT implementation
  Static NAT
    Each Private IP is fixed a public IP address
    Primarily done for Public facing servers and devices that interact with non-IP protocols
  Dynamic NAT
    A pool of IP is reserved for Translation
    Private IP connecting to Internet use one IP from the pool on a first-come first-serve basis
  Port address translation (PAT)
    One IP is used to NAT a group of private IPs

## Slide 52: Routing Protocols
Autonomous Systems
  An autonomous system (AS) is a portion of the internetwork under the same administrative authority.
  A unique ASN is allocated to each AS for use in BGP routing.
Routing Protocols
  Routing protocols were created for routers. These protocols have been designed to allow the exchange of routing tables, or known networks, between routers
The two main types of routing: Static routing and Dynamic routing
  Dynamic Routing Protocol
    Dynamically discover and maintain routes
    Calculate routes, Distribute routing updates to other routers
    Reach agreement with other routers about the network topology
  Static Routing Protocol
    Statically programmed routers send data over routes defined by the network Administrator.
Route Flapping
  Occurs when a router alternately advertises a destination network via one route then another (or as unavailable, and then available again) in quick sequence.
Blackhole
  A null route (blackhole route) is a network route (routing table entry) that goes nowhere.

## Slide 53: Dynamic Routing Protocols – Distance Vector
Routes are advertised as vectors of (distance, direction), where distance is defined in terms of a metric and direction is defined in terms of the next-hop router.
each router learns routes from its neighbouring routers' perspectives and then advertises the routes from its own perspective.
Distance vector routing is sometimes referred to as "routing by rumor.“
Distance vector routing protocols include the following:
  Routing Information Protocol (RIP) for IP
  Xerox Networking System's XNS RIP
  Novell's IPX RIP
  Cisco's Internet Gateway Routing Protocol (IGRP)
  AppleTalk's Routing Table Maintenance Protocol (RTMP)

## Slide 54: Link State Routing Protocol
The basic concept of link-state routing is that every node constructs a map of the connectivity to the network, in the form of a graph, showing which nodes are connected to which other nodes.
Each router in the network keeps a copy of it, without changing it. After obtaining the complete picture of network topology, each router will independently calculate its own best paths to reach the destination networks.
Link state protocols are based on Shortest Path First (SPF) algorithm to find the best path to a destination.
Shortest Path First (SPF) algorithm is also known as Dijkstra algorithm.
Whenever a link's state changes, a routing update called a Link-State Advertisement (LSA) is exchanged between routers
When a router receives an LSA routing update, the link-state algorithm is used to recalculate the shortest path to affected destinations.
Examples of link state routing protocols are:
  Open Shortest Path First (OSPF) for IP
  Novell's NetWare Link Services Protocol (NLSP)

## Slide 55: Distance Vector Vs Link State
Distance Vector | Link State
Distance Vector router tells ONLY neighbours about ALL routes | Link-State router tells ALL other routers about ONLY its neighbors and links
With Distance Vector protocols a router can't send out new vectors until it has processed them | In Link-State protocols Update and Decision processes are independent
 | Displays faster convergence than distance vector routing protocols
 | More scalable due to hierarchical nature
 | Require more memory to store state information

## Slide 56: Interior vs Exterior Routing Protocols

## Slide 57: Interior Routing Protocols
Routing Information Protocol
  It is a distance vector protocol
  Considered a legacy protocol (slow performance and lack of functionality)
  Should be used only within small networks
  V1 has no authentication
  V2 sends passwords in clear text or MD5 Hashed
  V3 supports IPV6

## Slide 58: Interior Routing Protocols
Open Shortest Path First (OSPF)
  It is a Link state protocol
  Uses LSA to send out routing table information
  Provides more stable network than RIP
  Requires more memory and CPU resources
  Allows for hierarchical routing network
  OSPF V3 uses IPSec for authentication

## Slide 59: Interior Routing Protocols
Interior Gateway Routing Protocol (IGRP)
  It is a Distance Vector protocol
  Cisco Proprietary
  IGRP is intended for use in gateways connecting several networks.
  The metrics used by IGRP include the following:
    Topological delay time - the amount of time it would take to get to the destination along that pat
    Narrowest bandwidth segment of the path - the bandwidth in bits per second of the slowest link in the path.
    Channel occupancy of the path - indicates how much of that bandwidth is currently in use
    Reliability of the path - It is the fraction of packets that arrive at the destination undamaged.

## Slide 60: Interior Routing Protocols
Enhanced Interior Gateway Routing Protocol (EIGRP)
  Cisco-proprietary Hybrid routing protocol, incorporating features of both Distance-Vector and Link-State routing protocols.
  EIGRP will form neighbour relationships with adjacent routers in the same Autonomous System (AS).
  EIGRP traffic is either sent as unicasts, or as multicasts on address 224.0.0.10, depending on the EIGRP packet type.
  EIGRP routers do not send periodic, full-table routing updates. Updates are sent when a change occurs, and include only the change.
  EIGRP supports IP, IPX, and Appletalk routing.

## Slide 61: Interior Routing Protocols
Virtual Router Redundancy Protocol (VRRP)
  Used in networks that cannot tolerate router single point of failure
  Used in router HA
  Designed to increase the availability of the default gateway
  A virtual router is advertised as default gateway and two routers are mapped to the virtual router, acting as redundant pairs
Intermediate System to Intermediate System (IS-IS)
  Link State protocol
  Similar to OSPF builds database of network topology
  Vendor neutral classless and hierarchical routing protocol
  Does not support IP address

## Slide 62: Exterior Routing Protocol
Exterior Gateway Protocols handle routing outside an Autonomous System
Border Gateway Protocol (BGP) is a routing protocol used to transfer data and information between different host gateways, the Internet or autonomous systems.
BGP is a Path Vector Protocol (PVP), which maintains paths to different hosts, networks and gateway routers and determines the routing decision based on that.
  It uses both Link state and Distance vector routing routing algorithms
  Creates a network topology using Link state functionality
  Propagates the updates a periodic intervals similar to Distance Vector routing

## Slide 63: Networking Devices

## Slide 64: Repeaters
Works at the physical layer
Does not understand IP or MAC address
Helps extend the network connections by extending the signals between cable segments
Helps amplify signals
  Works best for Digital signals than analog signals
Hub is a multi-port repeater
Broadcasts packets to all ports

## Slide 65: Bridges
Works at the Datalink layer (MAC address)
Works with frames
Helps amplify signals
Segments a large network into smaller networks
3 main type of bridges
  Local: Connects two LAN segments with a local area
  Remote: Connects two LAN segments over a MAN
  Translation: Connects two LAN segments using different types and standards
Broadcast Storm:
  Bridges can forward broadcast traffic causing a network or broadcast storm

## Slide 66: Transparent Bridging
A bridge that observes incoming network traffic to identify media access control (MAC) addresses.
Transparent bridge records MAC addresses in a table that is much like a routing table and evaluates that information whenever a packet is routed toward its location.
The algorithm has five parts:
  Learning
  Flooding
  Filtering
  Forwarding
  Avoiding loops

## Slide 67: Spanning Tree Algorithm
Spanning Tree Protocol (STP) is a Layer 2 protocol that runs on bridges and switches.
Implemented on bridges and switches in order to prevent loops in the network
The algorithm is responsible for a bridge using only the most efficient path when faced with multiple paths.
The spanning tree algorithm determines the network (which computer hosts are in which segment) and this data is exchanged using Bridge Protocol Data Units (BPDUs).

## Slide 68: Source Routing
Technique whereby the sender of a packet can specify the route that a packet should take through the network.
It is assumed that the source of the packet knows about the layout of the network and can specify the best path for the packet
A common form of source routing is called loose source record route (LSRR). When using LSRR the sender will provide one or more hops that the packet must go through.
This is dangerous because it allows the sender to bypass control points.

## Slide 69: Switch
Combines the functionality of the repeater and bridge
It’s a multiport bridge
Works at Layer 2, but there are switches that can work upto Layer 4
Prevents collision domains and reduces broadcast
Switches that work at layers beyond 2 are called as multi-layered switches
  They use hardware-based processing power to offer routing functionality, packet inspection, QoS etc.

## Slide 70: Switch – Tags/Label (MPLS)
Layer 3 and 4 Switches use a concept called tags to route traffic
Tags are assigned to each network or subnet and the information is stored in the switches
When a packet reaches the first switch, the destination is verified and the tag is mapped
From now on, every other switch will just look at the tag and route the traffic instead of analysing the complete header information
This ensures efficient routing and also helps in setting labels for different priority data

## Slide 71: VLAN
A VLAN is a group of devices on one or more LANs that are configured to communicate as if they were attached to the same wire
VLAN controls the broadcast without the use of layer 3 devices.
Switch ports are operate in 2 different modes; Access and Trunks.
  Access ports: are those which carry the traffic of only one VLAN.
  Trunk ports: It carries multiple VLANs at a time. Unlike access ports when the switch forwards a frame out the trunk interface it adds VLAN tagging information.

## Slide 72: VLAN Hopping Attacks
The basic concept behind all VLAN hopping attacks is for an attacking host on a VLAN to gain access to traffic on other VLANs that would normally not be accessible.
There are two primary methods of VLAN hopping: switch spoofing and double tagging
Switch spoofing: An attacking host imitates a trunking switch by speaking the tagging and trunking protocols used in maintaining a VLAN. Switch spoofing can only be exploited when interfaces are set to negotiate a trunk.
Double tagging attack: A double tagging attack begins when an attacker sends a frame connected to a switch port using two VLAN tags in the frame header. If the attacker is connected to an 802.1Q trunk port, the first tag matches that of the native VLAN (usually 1). The second tag identifies the VLAN the attacker would like to forward the frame to.

## Slide 73: Router
Layer 3 device
Works with packets
Helps interconnect different segments, network or VLANs
Controls broadcast as well as collision domains
Controls access between segments via ACLs
Performs Address Translation

## Slide 74: Gateway
Gateways regulate traffic between two dissimilar networks, while routers regulate traffic between similar networks
Gateways perform more complex functions than the router
Eg: connect voice and data network; connect IPX with IP network

## Slide 75: Firewalls
Used to restrict access to one network from another network
Considered chock points in the network
Work from Layer 3 to Layer 7
Different types
  Packet filtering
  Stateful
  Proxy
  Dynamic Packet filtering
  Kernel Proxy
3 different firewall architectures
  Screened host
  Multihomed
  Screened subnet

## Slide 76: Packet Filtering Firewall
Works in Layer 3 and 4
Stateless firewalls
Takes decision based on source and destination IP/Port numbers, protocol type and direction
Advantage | Disadvantage
Not application dependent | Cannot prevent attacks that attack application specific vulnerabilities
Scalable | Has limited logging facilities
Have high performance | Do not support identity based access
Commonly used as first line of defence | Cannot detect spoofed address
 | May not be able to detect fragmentation attacks

## Slide 77: Stateful firewalls
Maintains a state table of all connections; only the first packet is deep inspected, subsequent connections are not inspected
Provides high degree of security and does not introduce the performance hit
It is scalable and transparent to the user
Provides data for tracking connectionless protocols

## Slide 78: Proxy Firewalls
Intercepts and inspects the packets before it is delivered to the destination
It breaks the connection between the peers
Two types of proxies
  Circuit Level Proxy
  Application Layer Proxy

## Slide 79: Circuit-level Vs Application Layer Proxy
Circuit-level Proxy | Application Layer Proxy
Works at the session layer | Works at the application layer
Cannot look into the contents of the packet | Has visibility to the entire packet
Takes decision based on the header information | Takes decision based on the content of the packet
It is application independent | Has one proxy per protocol
SOCKS is a circuit level proxy | Capable of authenticating users directly
 | Has performance issues due to deep inspection

## Slide 80: Dynamic Packet Filtering
Helps in creating dynamic ACLs for connections initiated from internal networks
Return traffic is allowed based on the dynamic source port combinations
Helps prevent creating multiple ACLs in the firewall

## Slide 81: Kernel Proxy firewalls
5th generation firewall
It creates dynamic, customized network stacks when a packet needs to be evaluated
The packet is scrutinized at every layer of the protocol stack and action is determined
It breaks the connection between the peers (proxy)
Faster than application proxy firewalls
Can perform NAT functionality

## Slide 82: Firewall Architecture
Dual-Homed Firewall:
  A device that has two interfaces connecting to two different segments, controlling traffic flow
  The device should not perform packet forwarding and routing functionalities
Screened Host:
  A device that is connected to the Internet router; segregating the Internal network
  Traffic from the Internet router can only connect to this firewall; after inspection it is passed on to the internal network
Screened Subnet:
  Adds another layer of protection to the screened-host architecture
  Instead of routing traffic from the internet after screened host firewall, the connection passes through another firewall
  This creates DMZ segment in the network
  Provides multiple layer protection

## Slide 83: Firewall best Practices
Silent Rule: Drop noisy traffic without logging
Stealth Rule: Frist rule, block connections targeting the firewall
Cleanup Rule: Last rule, drops and logs all traffic that does not meet the preceding rules
Negate Rule: provide access only to the required needs.

## Slide 84: Proxy Servers
Acts as intermediary between clients that need to communicate
Caches the responses it receives so that requests from other clients are served faster
Forwarding proxy: Forwards connections from the clients to the intended destinations; helps perform URL filtering, malware protection, data loss prevention
Reverse Proxy: Acts as intended servers the clients try to connect to; can perform load balancing, encryption, caching

## Slide 85: Honeypot
A computer that is intended to be exploited by attacker
Usually sits in the screened subnet
Should not be directly connected or be a jump host to internal network
Helps understand the strategies targeted by the attacker
Two or more honeypots combined together to form Honeynet
Tarpit is a type of honeypot that provides protection against automated scanners by delaying the responses to be timed-out

## Slide 86
Karthikeyan Dhayalan
MD & Chief Security Partner
www.cyintegriti.com